## Slide 1: Customer Requirements
Divided into three different sections
  High priority: Must be implemented for project to be accepted
  Medium priority: Nice to have. Should fulfill as many as possible
  Low priority: Least important. Implement if time permits

## Slide 2: Customer Requirements High Priority
The system shall contain a camera to monitor areas of interest
The camera shall be capable of panning
The camera shall be controllable via user’s mobile device
The camera’s video feed shall be accessible from the user’s mobile device
The system shall contain sensors to detect motion on the property
The system shall notify the user when a sensor is triggered
  User must be connected to the Internet
The system shall allow users to dial 911 with the touch of one button
  User must be connected to cellular network
The user shall be able to define zones that the camera can automatically pan to based on the triggering of sensors
  Specified zones must be reachable by the camera

## Slide 3: Customer Requirements High Priority
The system shall save a log of triggered events on the central computer
The user shall be able to set up profiles that specify the severity of a triggered event
The user shall be able to set up notification profiles on their mobile device that establish how to react to notifications concerning certain triggered events
The MAVS System shall require user authentication for accessing camera functions, such as audio/video
  Store passwords securely, no plain text
The camera shall track the subject that has triggered the sensors, as long as the subject is within the camera’s view
  The ability for the camera to continuously track the subject is constrained by the amount of sensors available. The exact mechanism for tracking will be determined in the System Architecture phase.

## Slide 4: Customer Requirements Medium Priority
The system shall be able to incorporate additional sensors, regardless of type
  Sensors must be compatible with IC
The system shall support two-way audio
  Constraint assumes camera support
The system shall handle user unavailability
  Only possible if other users allowed access to system
The system’s mobile application shall alert the user when connectivity to the central computer is lost
The user shall be able to view archived video footage on the central computer

## Slide 5: Customer Requirements Low Priority
The system shall notify the user when it has lost its main power source
  The system must be hooked up to backup power

## Slide 6: Acceptance Criteria
For the project to be accepted, the previous high priority requirements must be fulfilled and all safety requirements must be met

## Slide 7: System Constraint Requirements
The camera shall not operate in the rain
  Derived from limited resources and budget
The system shall operate on AC power
  Recommended to have backup UPS power if main power source is down
    Access to the camera feeds and options shall only be accessible when the user has a connection to the Internet
      There will be no other means to communicate between the central computer and mobile device

## Slide 8: System Constraint Requirements
The MAVS System shall save video to the central computer only as long as there is enough disk space to hold it
  Hurrr durrrrr